## Slide 1
Approved for public release; distribution is unlimited.
INL-CON-25-84243
Expansion of the Fast Neutron Hodoscope at TREAT to Support Fuel Safety Experiments
David Chichester
James T. Johnson
Jay D. Hix
Jeff S. Burggraf
Luis A. Ocampo Giraldo
Scott J. Thompson
Tommy V. Holschuh
The work presented here is sponsored by the U.S. DOE Office of Nuclear Energy's Advanced Fuels Campaign and the Nuclear Science User Facilities.

## Slide 2
Arial View of the Transient Reactor Test (TREAT) Facility
Air-cooled, graphite moderated thermal reactor
100 kW steady-state power; 19 GW peak transient power
Core
  1.2 m high x 1.9 m square
  Surrounded by 0.25 m graphite reflector
Fuel
  Highly-enriched uranium
  0.225 wt.% (100 ppm) UO2 dispersed in graphite
12 steady-state control rods and 8 transient control rods
Instantaneous, large negative temperature coefficient (self protecting driver core)

## Slide 3: Transient Experiments at TREAT
Three-dimensional rendering of the TREAT core, illustrating the fuel elements (grey) and the transient test vehicle (orange)
Leak-tight secondary enclosure
Individual fuel-rod in test capsule

## Slide 4: Transient Experiments at TREAT
The key measurement at TREAT: monitoring the movement and relocation of fuel
Method: fast-neutron hodoscope
A row of fuel elements is left empty between the fuel and the outside
A fast-neutron collimator with hundreds of small slits is placed external to the core, each viewing a small area of the test vehicle
Fast neutron detectors are placed at the outside surface of the collimator
Fission is induced in the fuel sample by the reactor during the transient
Fission-neutrons from the test specimen leak from the core, through the slits, and are measured in the detectors
Three-dimensional rendering of the TREAT core, illustrating the fuel elements (grey) and the transient test vehicle (orange)
Fast-neutrons from fission occurring in the test specimen

## Slide 5: TREAT Fast-Neutron Hodoscope

## Slide 6: 2024 Expansion
Prepared and installed 96 additional detectors
Detector efficiency studies
Prepared and installed new data acquisition system (DAS) cabinet (192 channels)
Commissioning tests - steady-state and transient

## Slide 7: New Detectors for Installation
There are 360 detector slots in the hodoscope collimator
Recent expansion from 96  192 slots filled with proton recoil scintillator detector (PRSD, aka Hornyak Buttons) – ZnS/epoxy matrix sandwiched between Lucite hemi-cylinders
Real-time neutron/photon discsitmaition using FPGA-based PSD
Data is recorded in 1-ms time bins
Maximum instantaneous data rate of ~400,000 events s-1

## Slide 8: Detector Efficiency Studies
Neutron ToF is used to determine neutron speed, and thus neutron energy
The well-known energy distribution of 252Cf neutrons is compared to our measured neutron energy distribution
This gives us the relative neutron efficiency as a function of energy
Relative energy-dependent neutron detection efficiency for six PRS detectors

## Slide 9: Detector Efficiency Studies
Neutron ToF is used to determine neutron speed, and thus neutron energy
The well-known energy distribution of 252Cf neutrons is compared to our measured neutron energy distribution
This gives us the relative neutron efficiency as a function of energy
Tests with a well-defined neutron source allow us to scale energy-dependent curves for absolute efficiency
The FMMS' PRS detectors were reported to have a detection efficiency for neutrons above 0.1 MeV of ~0.004 (0.4%) counts per incident neutron in this application.
Nucl. Tech. 27 (1975) 449-489
Absolute energy-dependent neutron detection efficiency for six PRS detectors

## Slide 10: New DAS Cabinets
New DAS cabinet
Stringing the cables out and testing for continuity
192 detector assemblies, each has an HV cable and a signal cable
Each cable is 100 feet in length
A total of 11 km of cables were laid out during the 192-detector expansion
Laying new cables

## Slide 11: Commissioning Tests
Verification tests are performed to confirm each detector is functioning and in the correct location
A PuBe source is placed in the XY translation system near the detector cabinet and scanned over the entire detector cabinet
A machine learning engine adjusts the bias voltage to normalize the count rates
The gamma-ray count rates, PSD FOM, and final bias voltages are determined

## Slide 12: Reactor Tests
The reactor was operated at a constant power of 80 kW
Steady state operation allows monitoring each detector’s performance metrics
Transient testing allows assessment for dynamic range and identification of outliers
Reactor steady-state test give flat-field image for normalization
Reactor transient test for dynamic range assessment

## Slide 13: Hodoscope Data Visualization - Fuel Experiment
A transient test with a fresh LEU fuel rodlet

## Slide 14: Summary
The Fuel Motion Monitoring System (Hodoscope) at the TREAT reactor was expanded from 96 channels to 192 channels
Research continues to improve our understanding of the PRS detectors used to monitor neutrons in the Hodoscope
Looking towards 2025 TREAT will be studying a variety of fuels and transient accident scenarios, with an emphasis on LOCA
The Hodoscope can provide key information needed to understand accidents and qualify new fuel
  Axial fuel swelling rate
  Time and location of clad rupture
  Fuel density changes due to fracture, rubbleization, and relocation
  Fuel relocation time and mass
  Water height level during LOCA
  RIA accident progression
  Dynamic power coupling factor and fuel axial heat generation rate

## Slide 15
15